## Slide 1: SDMI Source Imagery Collection
Updating Alaska’s image maps
Drew Hopwood
February 24, 2011

## Slide 2
Airbus
Eurocopter
Cassidian
Astrium
Space Transportation
Astrium Satellites
GEO-Information
Telecommunications
Secure Satcom Systems
Navigation
Astrium Services
GEO-Information Services within Astrium and EADS

## Slide 3: Corporate Overview
Spot Image
Corporation
Spot Image
Brasil
Spot Imaging
Services
Spot Asia
Beijing
Spot Image
Tokyo
Spot Image
Infoterra Spain
Spot Image
Infoterra UK
Infoterra
Germany
Infoterra Hungary
Spot Infoterra Hellas
Infoterra AP
Strong Global Presence
  Staff: +900, located in 12 countries
  North American office located in Chantilly, VA
Balanced Portfolio
  Optical & Radar Geo-Imagery
  Change Detection & Monitoring Services
  Global, Highly Accurate DEMs
Extensive Satellite & Imagery Resources
  Satellites in Operation: SPOT 4 & 5, TerraSAR-X & TanDEM-X
  World’s Most Extensive Network of Direct Receiving Stations
  Upcoming Very High-Resolution Satellites: Pléiades 1 & 2
  SPOT 6 & 7 Continuity Program
  Distribution Rights for Other Satellites: FORMOSAT-2, KOMPSAT-2, DEIMOS-1

## Slide 4: Optical & SAR Imagery
SPOT-4 & -5
2.5m -20m Optical Data
60km x 60km Image Swath
100+ Billion km2 Archive
Pléiades-1 & -2
50cm Optical Data Products
Daily Revisit
95% of Resources Dedicated to the Commercial Market
FORMOSAT-2
2m Optical Data
Daily Revisit
Great for Site Monitoring
KOMPSAT-2
1m Optical Data
Image Swath
Very High Resolution Large-scale Mapping
TerraSAR-X
SAR Imagery -
Up to 1m Resolution
Weather-independent
Unrivalled Access
DEIMOS-1
22m Optical Data
600km Image Swath
Daily Revisit
Cloud-free coverage of the UK in two images!

## Slide 5: Elevation Datasets
Reference3D
DTED-2
Ortho Image & Quality Masks
120+ Million km2 Coverage
LiDAR
DEM, DTM, DSM
10cm – 2m Posts
Sub-meter Accuracy
SPOT DEM
20m Post Spacing
49 Million km2 Off-the-shelf
TanDEM-X
Satellite IFSAR DEM
Global Collection Plan
High Accuracy
TerraSAR-X
Radargrammetry DEM
10m Post Spacing
Weather-independent
Unrivalled Access
HR Stereo Pairs
Satellite or Aerial based data
High Accuracy
On Demand Processing

## Slide 6: Hybrid Elevation Solutions
SPOT DEM
TerraSAR-X DEM
Void Free DEM

## Slide 7: Hybrid Elevation Solutions
SPOT DEM
TerraSAR-X DEM
Hybrid DEM
Increased coverage over cloudy regions
Cost effective
Constant quality

## Slide 8
Mapping &
Land management
Environment &
Forestry
Defense & Security
Risk & crisis
management
Oil & Gas, Mines
LBS &
Navigation
Agriculture
Maritime & coastal
Serving Versatile Application Needs

## Slide 9
SPOT-5
  2 High Resolution Geometry (HRG) Instruments
    2.5m & 5m Panchromatic
    10m 4-Band Multispectral
      Green, Red, NIR, & SWIR
  High Resolution Stereo (HRS) Instrument
    DTED-2 DEM (Reference3D)
    20m Post Spacing DEM (SPOT DEM)
  Vegetation (VGT) Instrument
HRS
HRG1
HRG2
VGT
SDMI Ortho Imagery Source
  2.5m Pan & 10m MS Scene Bundles
US Forest Service
  Copper River Delta Project
  HRS DEMs in the Chugach and Tongass National Forests
Woods Hole Research Center & UAF
  Vegetation Responses to Climate Change
    More information http://www.planet-action.org/web/85-project-detail.php?projectID=1571
SPOT 5 in Alaska

## Slide 10: SDMI Source Imagery Requirements
Collect Upland Alaska
  ~1.56m km2
  ~900 SPOT-5 scenes
Sun Angle Above 30º
  Shortens Collection Season in Northern Areas
Leaf-on
Less than 10% clouds
  Also Cloud Shadow, Hazy, Smoke & Snow
Ortho Accuracy 1:24k
  Collection Limit: +/-15º Off Nadir

## Slide 11: Current Source Imagery Collection Status
Collected 294 Scene Bundles
Covering 603,000km2 or 39% of Alaska

## Slide 12
Collected
Delivered
2010 Collection Overview
Bundles Collected | 1271
Bundles Delivered | 210
Delivery Percentage | 16%
Chart: Data Acquired in 2010 by Month
| May* | June | July | August | September
Collected | 75 | 308 | 290 | 260 | 338
Factors Limiting 2010 Delivery
  Clouds
  Sun Angle

## Slide 13: Clouds
More Challenging Than Anticipated
  July was the most challenging
    From July 14 to August 1, no imagery was delivered because of heavy clouds.
  Conditions improved in September
Chart: Percent Delivered to Collected
| May* | June | July | August | September
Validate to Collected each month | 0.12 | 0.18506 | 0.11379 | 0.12692 | 0.23077
Chart: Bundles Delivered by Month
| May* | June | July | August | September
Validated | 9 | 57 | 33 | 33 | 78
16%

## Slide 14: Sun Angle
Starting in September, the sun angle requirement limited the amount of deliverable data bundles.
Clearing weather conditions in September increased the amount of near cloud-free scene bundles being collected; however, the sun angle requirement prevented them from being delivered.
  In total, 111 scene bundles were collected, which met all delivery criteria except the sun angle.
  Increased total coverage to 48%
Chart: Addition of Low Sun Angle Bundles by Month
| May* | June | July | August | September
Delivered | 9 | 57 | 33 | 33 | 78
Low Sun Angle | 0 | 0 | 0 | 0 | 111

## Slide 15: 2011 Collection Season
Anticipated Delivery: 200 – 300 Scene Bundles
Complete Collection of the North Slope
Gather Input On User Priorities
  Discussion Friday Morning

## Slide 16
Astrium GEO-Information Services
Drew Hopwood 14595 Avion Parkway, Suite 500 Chantilly, VA 20151 (703) 715-3100

## Slide 17: TSX/HRS DEM MERGING

## Slide 18: TSX/HRS DEM MERGING