## Slide 1
Alaska Sources of Control – SDMI Task 4
Notes: <number>

## Slide 2: Goal & Approach
Conduct a survey of existing control sources.
Public and private sources that could be acquired for Alaska utilization.
Separate existing image identifiable content
Also gather pragmatic feedback from existing practitioners
Produces maps and report

## Slide 3: Just because you’ve got it doesn’t mean it’s the right fit for the job

## Slide 4: What is the Application
  Geodesy, Costal, Civil Engineering?
  Aviation?
  Control imagery?
    1:24k NMAS
    EO or RaDAR
  Correlate with other datasets?
    Change detection, veg mapping, EIS?
  Control DEM?
  Validate imagery or DEM?
  Control collection platform?

## Slide 5: 45km Populated Places Buffers Approx. 63% of Alaska

## Slide 6: 45km Runway Buffers Approx. 63% of Alaska

## Slide 7: Some Variables
  Desired map scale / accuracy of output products
  Interaction with other input components
  Error budget
  Image identifiability
  Orientation related to area of mapping
  Stability over time (seasons and years)
  Costs of collection
  Access
  Costs of utilization

## Slide 8: Approximate Map Scale Equivalencies
Map Scale | CE90 | RMSE | 1-Sigma
1:50,000 | 25.4m | 15m | 12m
1:24,000 | 12.2m | 6m | 3m
1:12,000 | 10.2m | 5m | 2m
1:4,800 | 4.1m | 2m | 2m
1:2,400 | 2.0m | 1m | 1m

## Slide 9: Imagery Ortho Error Budget
Many factors contribute to the overall accuracy of map product
  DEM
  Incidence angle, sensor to ground
  GCP
  Sensor design
  Orbital Position Estimation
  AGPS & IMU / Pointing Accuracy
  Block size

## Slide 10: DEM Accuracy is Significant Error Source for Imagery Location

## Slide 11: Error Budget Calculations

## Slide 12: GCP Accuracy
Keep mapping scale in mind
1:24K means a 0.1mm thick line is 2.4m wide on the ground!
To achieve NMAS, >90% of all sample points must fall less than 40 feet (12.19m) from ground truth

## Slide 13: GCP Accuracy
Most modern survey grade GNSS receivers capable of +/- 5mm + 0.5ppm (1 sigma)
CORS may provide sufficient coverage if SDMI requirements are 1:24,000

## Slide 14: CORS Availability

## Slide 15: Alternatives to CORS - UNAVCO

## Slide 16: Alternatives to CORS
TerraPOS – uses precise GPS satellite ephemeris

## Slide 17: GPS and GNSS
Raise elevation mask 2⁰/100km from base to ensure common satellites observed
If possible, use a GNSS receiver rather than straight GPS – better for mountains

## Slide 18: Satellite Imagery as Control (all CE90)
Sensor | Native Radial Accuracy | Improved Accuracy
SPOT 5 | 39m | 15m w/ Ref3-d
IKONOS | 15m | 
Quickbird | 23m | 
WorldView-1 | 6.5m modeled | 3m – 5m actual
GeoEye-1 | 5.0m modeled | 4m stereo, expect 2-5m mono actual