## Slide 1: Alaska National Elevation Dataset (NED)
  Seamless raster mosaic
  Consistent national coordinate system
  Standardized datums and units
  Filtered and edge-matched, where necessary
  Spatially referenced metadata

## Slide 2: The National Elevation Dataset (NED)
Seamless national coverage of “best available” public domain raster elevation data
  Geographic “projection”
  Datum: NAD 83 horizontal; NAVD 88 vertical
  Elevation units: decimal meters
  1-arc-second (30-meter), 1/3-arc-second (10-meter), and 1/9-arc-second (3-meter) grid spacing
    Alaska: 2-arc-second grid spacing
  Updated bi-monthly to incorporate all new USGS DEM production and other newly available source data

## Slide 4
Multi-resolution NED
1-arc-second (30 meters)
1/3-arc-second (10 meters)
1/9-arc-second (3 meters)

## Slide 5: NED Production Flow
Source data selection
Datum and unit conversion
Projection transformation and resampling
Artifact removal
DEM merge
Edge match
Metadata generation
Shaded relief generation
Inspection
NED

## Slide 6: NED Spatial Referenced Metadata
Polygon attributes store information about source DEM and NED processing

## Slide 11
Bulk data delivery
  Customer provides the hard drives
  Data format options are limited to ArcGrid or FloatGrid
  Turn around time may be 4-8 weeks
  All the data for the customer’s specific resolution will be placed on the hard drive
  Possible exception for Alaska
  Send requests to: bulkdatainfo@usgs.gov

## Slide 12: USGS Seamless Server
  pro - standardize seamless product with spatial metadata
  pro – offers both customer defined area download and bulk deliver
  pro - higher resolution source data is used to improve lower resolutions layers
  con- data is modified from original state
  con - download data is chipped into 250mb pieces requiring remosaicking
  con – bulk delivery output formats are limited to ArcGrid and FloatGrid

## Slide 13: Useful links:
http://seamless.usgs.gov
http://ned.usgs.gov
http://ned.usgs.gov/Ned/downloads.asp