## Slide 1: Reference3D-- DTED2 DEM Product
Foundation Data Set for Alaska
Notes: <number>

## Slide 2: What is Reference3D ?
Ref3D is a package of the 3 components produced out of the data collected by the High Resolution Stereo (HRS) sensor on the SPOT 5 satellite, and supplemented with High Resolution Ground (HRG) in steep areas. The product is especially designed for large area coverage.
© Spot Image 2008
<number>
Metadata
Ortho Image
DEM (Elevation data）
DTED2 format , 10m LE90
elevation data at 1 arc second posting (~30m)
CIB5 equivalent, 16m CE90
Panchromatic ortho-image with 1/6 arc second (~5m) resolution
Quality information layers ・Date, source… ・Quality info : reliability, effective accuracy,…
Product Unit：1°×1° geocell
No need for GCPs
Alaska Dem Workshop
Notes: <number>
Re3Dの定義
  Reference 3D = DTED2 レベルのDEM+ CIBライクのオルソ画像
  精度
  Re3DのDEM CE（絶対） 15m LE（絶対） 10m
  SRTM CE 30m LE 16m
  Re3Dのオルソ CE（絶対） 16m
  QBのオルソ（1:5万） CE 25.4m
  （1:1.2万） CE 10.2m

## Slide 3: In what kind of format is the product delivered?
© Spot Image 2008
<number>
We use a DIMAP format, which is an XML-based hierarchical file structure. We do this so that all the elements of the Ref3D product can be easily encapsulated into a simple software structure and viewed by any generic browser, such as Microsoft Internet Explorer or Firefox.
Alaska Dem Workshop
Notes: <number>
Re3Dの定義
  Reference 3D = DTED2 レベルのDEM+ CIBライクのオルソ画像
  精度
  Re3DのDEM CE（絶対） 15m LE（絶対） 10m
  SRTM CE 30m LE 16m
  Re3Dのオルソ CE（絶対） 16m
  QBのオルソ（1:5万） CE 25.4m
  （1:1.2万） CE 10.2m

## Slide 4: In what kind of format is the product delivered?
© Spot Image 2008
<number>
Screen shot of Microsoft Explorer, with a Ref3D DIMAP product open. You can click on the various products and tabs to view the individual product components.
Alaska Dem Workshop
Notes: <number>
Re3Dの定義
  Reference 3D = DTED2 レベルのDEM+ CIBライクのオルソ画像
  精度
  Re3DのDEM CE（絶対） 15m LE（絶対） 10m
  SRTM CE 30m LE 16m
  Re3Dのオルソ CE（絶対） 16m
  QBのオルソ（1:5万） CE 25.4m
  （1:1.2万） CE 10.2m

## Slide 5: Parts is Parts—The DEM Itself
© Spot Image 2008
<number>
Screen shot from RemoteView, with the DEM (.DT2 file) displayed in a 16 layer color palate, based on elevation values. The geocell is N35E110, a region in central China. The Luo River flows from north to south out of a mountainous area and onto an open plain.
Alaska Dem Workshop
Notes: <number>
Re3Dの定義
  Reference 3D = DTED2 レベルのDEM+ CIBライクのオルソ画像
  精度
  Re3DのDEM CE（絶対） 15m LE（絶対） 10m
  SRTM CE 30m LE 16m
  Re3Dのオルソ CE（絶対） 16m
  QBのオルソ（1:5万） CE 25.4m
  （1:1.2万） CE 10.2m

## Slide 6: Parts is Parts—The Water Mask
© Spot Image 2008
<number>
Water mask of N35E110, an area in central China. The Ref3D product comes with a total of eight quality masks, the water mask is one of the eight.
Alaska Dem Workshop
Notes: <number>
Re3Dの定義
  Reference 3D = DTED2 レベルのDEM+ CIBライクのオルソ画像
  精度
  Re3DのDEM CE（絶対） 15m LE（絶対） 10m
  SRTM CE 30m LE 16m
  Re3Dのオルソ CE（絶対） 16m
  QBのオルソ（1:5万） CE 25.4m
  （1:1.2万） CE 10.2m

## Slide 7: Parts is Parts—Other Masks
© Spot Image 2008
<number>
Correlation Mask (MCo)
Cloud/snow Mask (MCl)
Exogenous Mask (MEx) —Areas where other DEM
data has been inserted
Regulation Mask (MRe) —Where interpolation
has been done to fill in voids
Quality Mask (MQu)—Based on the manual assessment
of an operator
Merge Mask (MMe)—Shows areas of overlap boundaries for the
HRS strips that make up the coverage in a one degree geocell
MVa Mask—Sum of MQu + MRe + MCl + MEx = MVa
Alaska Dem Workshop
MCo
MMe
Notes: <number>
Re3Dの定義
  Reference 3D = DTED2 レベルのDEM+ CIBライクのオルソ画像
  精度
  Re3DのDEM CE（絶対） 15m LE（絶対） 10m
  SRTM CE 30m LE 16m
  Re3Dのオルソ CE（絶対） 16m
  QBのオルソ（1:5万） CE 25.4m
  （1:1.2万） CE 10.2m

## Slide 8: Parts is Parts—The Orthomosaic
© Spot Image 2008
<number>
Screen shot using RemoteView to show a portion of the orthomosaic.
Alaska Dem Workshop
Notes: <number>
Re3Dの定義
  Reference 3D = DTED2 レベルのDEM+ CIBライクのオルソ画像
  精度
  Re3DのDEM CE（絶対） 15m LE（絶対） 10m
  SRTM CE 30m LE 16m
  Re3Dのオルソ CE（絶対） 16m
  QBのオルソ（1:5万） CE 25.4m
  （1:1.2万） CE 10.2m

## Slide 9: Reference3D Product—Some Additional Details
Source electro optical (EO) data comes from the High Resolution Stereo (HRS) instrument, operational on the SPOT 5 satellite
In mountainous areas High Resolution Ground (HRG) imagery is also collected at Nadir, to enhance elevation extraction and prevent blind spots.
Broad area along-track stereo image collection. Each HRS strip pair is 120 KM wide by 600 KM long.
All processing is done without Ground Control Points (GCPs)
Absolute horizontal accuracy is 15 M CE90, or better
Absolute vertical accuracy is 10-30 M LE90, depending on terrain slope
Output DEM file (.DT2) completely conforms to the National Geospatial-Intelligence Agency (NGA) Digital Terrain Elevation Data) DTED specification, level 2 data density
Like the SRTM DEM, Ref3D is a surface DEM, and NOT a bare Earth DEM.
Alaska Dem Workshop
© Spot Image 2008
<number>
Notes: bvjv,bn,bn,
<number>

## Slide 10: Geo-location accuracy of Reference3D
© Spot Image 2008
<number>
  Ref3D DEM accuracy
  Ref3D Ortho Image absolute accuracy
Accuracy verified by major independent users
 | Ref3D DEM | SRTM | NATO DTED2
Horizontal （CE90） | 15m (absolute） 10m (relative） | 20 m (abs.) | 23 m (abs.)
Vertical （LE90 ) | 10m-30m (absolute） 5m (relative） | 16 m (abs.) | 18 m (abs.)
Alaska Dem Workshop
Notes: <number>
SPOT5画像の位置精度は、50m以内。
SPOT5オルソの位置精度は、DEMにもよるが、30m以内。Re3Dを使えば、15m以内。

## Slide 11: Production of Ref3D
Very large blocks are mandatory to perform large- block bundle trigonometric calculation (explained in more detail later)
Dedicated production line at IGN Espace (part of the French Mapping Agency)
  Production line started in 2002
  5 year HRS/HRG collection plan is ongoing.
  In 2008 this plan will be renewed for another 5 years, throurgh at least 2013.
Products referenced to WGS84 (horizontal) and WGS84 EGM96 geoid (vertical)
30 M KM2 of R3D coverage through 2008, +70 M KM2 of coverage to be added during 2009-2013
Alaska Dem Workshop
© Spot Image 2008
<number>
Notes: <number>

## Slide 12: Current High Resolution Stereo (HRS) Coverage of Alaska
SPOT has been imaging Alaska for three years to collect HRS, which is the source imagery for Reference3D. Here is the coverage status as of June 2008, 76% of the state is covered:
© Spot Image 2008
<number>
Alaska Dem Workshop
Notes: <number>

## Slide 13: Current High Resolution Ground (HRG) Coverage of Alaska
© Spot Image 2008
<number>
This data is used to supplement the HRS data in areas of high slope
Alaska Dem Workshop
Notes: <number>

## Slide 14: SPOT 5 Satellite Platform
© Spot Image 2008
<number>
Alaska Dem Workshop
Notes: <number>

## Slide 15: The same pixel row is acquired twice from the same orbit, after 90 s Ground sampling is 5 M across track, and 10 M along track
© Spot Image 2008
<number>
HRS : the acquisition process
Stereo
T0 + 90 s
T0
120 km
max. 600 km
Alaska Dem Workshop

## Slide 16: Reference3D® accuracy assessed by major customers and labs
© Spot Image 2008
<number>
NGA:
  SRTM - Reference3D® cross comparison (2003)
  Reference3D evaluation over difficult reliefs (2006)
  CCAP evaluation of SPOT 5 satellite data (2006)
ISPRS: (Int’l Society for Photogrammetry and Remote Sensing - 2004)
European Commission: (2004)
Various National Mapping Agencies: DGIA (Australia), Oman, Belgium, Germany, and Norway.
USGS, Earth Sciences Division
Alaska Dem Workshop
Notes: <number>

## Slide 17: Vertical Statistical Evaluation Summary Ref3D and SRTM vs. High-Accuracy Ground Control Points, Done in 2006 (all values are in meters; approximately 200 pts per cell)
<number>
Cell ID (Relief Type) Vertical (Z) (DEM-GCP) Difference
(%High-Med-Low) Mean 90% error Mean 90%error
N30E33 (0-35-65) 0.59 5.40 -2.33 7.13
N30E32 (0-30-70) 3.44 3.50 2.71 2.28
N30E49 (0-15-85) 2.09 6.05 2.86 5.75
N29E48 (0-0-100) 0.84 4.34 6.33 6.16
N32E39 (0-40-60) 2.77 3.53 4.65 3.86
N33E35 (45-25-30) -0.17 6.58 1.83 6.35
N30E47 (0-0-100) -0.48 3.38 4.34 3.85
N30E48 (0-0-100) 0.70 4.05 5.88 3.99
N36E43 (25-25-50) 1.85 5.12 7.99 6.06
N32E48 (30-35-35) -0.69 5.26 6.61 7.21
N36E44 (90-0-10) -0.67 6.13 6.76 6.90
SRTM Ref3D/SPOT 5
NATIONAL GEOSPATIAL-INTELLIGENCE AGENCY
© Spot Image 2008
Alaska DEM Workshop
Notes: <number>

## Slide 18: Accuracy, circa 2008
Example is a project in northern Africa
  Absolute horizontal 10.05 M CE95, using
  Using SRTM DTED1 as a reference
  Absolute vertical 2.68 M LE90 with
  SRTM DTED1 as a reference
Alaska Dem Workshop
© Spot Image 2008
<number>
Mauritania Block Bundle
Notes: <number>

## Slide 19: Example of a large-block bundle:
© Spot Image 2008
<number>
View of the “Stan” large-block (purple area) in Asia. The block comprises 420 geocells, 4.5 M km². Other statistics: 270 HRS stereo pairs, 130 HRG imagery strips (for mountainous areas), and 26,000 imagery strip tie points. Large block bundles were created as part of project Alpha.
Alaska Dem Workshop
Notes: <number>
Re3Dの定義
  Reference 3D = DTED2 レベルのDEM+ CIBライクのオルソ画像
  精度
  Re3DのDEM CE（絶対） 15m LE（絶対） 10m
  SRTM CE 30m LE 16m
  Re3Dのオルソ CE（絶対） 16m
  QBのオルソ（1:5万） CE 25.4m
  （1:1.2万） CE 10.2m

## Slide 20: Reference3D Production and HRS Archive Status, as of June 2008
Reference3D produced geocells (off-the-shelf) - 2,900
Validated HRS stereo pair coverage - 122,189,502 KM2
Alaska Dem Workshop
© Spot Image 2008
<number>
Notes: bvjv,bn,bn,
<number>

## Slide 21: Quality control & assessment to ensure Ref3D meets requirements
© Spot Image 2008
<number>
How are Ref3D accuracy specifications verified and monitored?
Careful monitoring, plus numerous controls, performed by several independent entities
  CNES: SPOT 5 monitoring includes image geometry & radiometry
  IGN: Control steps during the Ref3D production process
  SPOT Image: Formal control of the geocells
  French MoD: V & V work performed by a dedicated cartographic unit
  Assessments by customers, such as the NGA
CNES Global range calibration sites
Alaska Dem Workshop
Notes: <number>

## Slide 22: Main uses of Ref3D
© Spot Image 2008
<number>
Multi scale mapping
Comprehensive tool for image orthorectification
Foundation data set for GIS systems performing cadastral analysis and land use planning
Precision guidance
Mission preparation and rehearsal
Foundation layer to register intelligence and targeting data
Alaska Dem Workshop
Notes: <number>
カバレッジ
⇒非公開だそう。（小林さん情報。仕様書は公開されているけど・・・）
GTOPO30は、DTED1と同等。
DTED2, CIB5互換→米軍ほか連合国とのインターオペラビリティに役立つ
縮尺1/50000の地図作製に十分な精度をもつ。R3Dから作製した地図はVMAP0、VMAP1より正確

## Slide 23: Reference3D is being used by the NGA to fill SRTM voids
Alaska Dem Workshop
© Spot Image 2008
<number>
Notes: bvjv,bn,bn,
<number>

## Slide 24: Example of a SRTM DEM cell with voids, N19E023
Alaska Dem Workshop
© Spot Image 2008
<number>
Notes: bvjv,bn,bn,
<number>

## Slide 25
© Spot Image 2008
<number>
ANDORRE
SPOT Ortho image
ANDORRE : a 100% automatic tool for orthorectification
SPOT Scene (1A)
Ortho image
16m CE90
Reference3D ®
DEM
10m LE90
Automatic
Location
Relief
Correction
Alaska Dem Workshop

## Slide 26: Homogeneity , consistency of customer’s product on Ref3D
© Spot Image 2008
<number>
Consistency of customer’s production based on Ref3D is assured
  Orthomosaic product
  Vectormap product etc…
Year 2004
Project
Year 2006
Project
Year 2005
Project
R3D
Ortho
Vector
Complete continuity ensured
Confirmed by users
Alaska Dem Workshop
Notes: <number>

## Slide 27: Means to monitor polar ice cap status, SPIRIT project
© Spot Image 2008
<number>
Alaska Dem Workshop
Notes: <number>

## Slide 28: Means to monitor polar ice cap status
© Spot Image 2008
<number>
SPIRIT Project, with contributions from the French space agency, CNES, Spot, and IGN Espace. The chief goals of this project are to:
Image 2.5 million sq.km. of the Arctic and Antarctic regions, covering glaciers, small ice caps and the coasts of Antarctica and Greenland.
Allow scientists around the world working on themes in line with the International Polar Year (IPY) to access the SPOT 5 HRS archive through a dedicated Web interface.
Distribute DEM products free of charge to research laboratories approved by CNES, to give them a baseline topography that until now has been lacking for studies of polar ice, so they can map change in these regions.
An initial imaging campaign in the Northern Hemisphere has already covered 830,000 sq.km of Arctic regions. The ongoing Antarctic campaign has set out with the aim of covering 2 million KM2 of the ice sheet.
Alaska Dem Workshop
Notes: <number>

## Slide 29: SPOT Offer for Alaska Coverage
Licensing:
  Option 1 “Regional Business User” or RBU
  Includes US federal government, state government, and local government entities
  Includes contractors, when working on projects for the above government entities
  Option 1 National Elevation Data (NED). We also refer to this option as “Public Release.”
Costs:
  Retail (list) cost from our product catalogue is $4.00 per KM2 for the DEM only
  Retail cost for the DEM + Ortho + Quality masks is $10.95 per KM2
  Quantity discounts apply, of course. Based on the binning ranges suggested, the total cost is in the $10 to 30 M bin for state-wide coverage, with flexible licensing.
Delivery time frame: 12 to 18 months from start of the project
Alaska Dem Workshop
© Spot Image 2008
<number>
Notes: <number>

## Slide 30: How Reference3D fits into the topology of Global DEM data sets
ETOPO5--5 minute (10 KM) grid 1988 public
GTPO30 --30 arc second (1 KM) grid 1997 public
Globe--30 arc second grid 1998 public
ACE GDEM--30 arc second grid 2003 public
SRTM DTED 1--3 arc second grid 2004 public
SRTM DTED 2--1 arc second grid ● not public data ● collected January 2000
distributed by the NGA, used by US and coalition partners to create GIS products supporting military and relief operations, production is ongoing
Reference3D--1 arc second grid production began in 2002, commercial, not public release, production will continue through at least 2013, one benefit--able to go back and redo areas, allowing change analysis
Future—TerraSAR-X + Tandem-X, IOC ~ 2011, estimated DTED level 3 fidelity, commercial, not public release, InfoTerra GMBH will be global data distributor
Future—COSMOS-Skymed , Sabrina/Prisma tandem satellite project, IOC ~ 2011, no information from ASI on resolution or coverage, data to be distributed through e-GEOS, the Italian company set up to distribute all products and services from the satellites
Alaska Dem Workshop
© Spot Image 2008
<number>
Notes: bvjv,bn,bn,
<number>

## Slide 31: Global DEM Topology, Continued
© Spot Image 2008
<number>
Availability of the DTED1 & 2 SRTM DEM
about the lower 10% of Alaska is covered
Alaska Dem Workshop
Notes: title, place and date
<number>

## Slide 32: In Conclusion
© Spot Image 2008
<number>
Hi-precision geo-spatial foundation data, consistent source data and production methodology, plus open standard data format
No need for external data such as GCPs
Homogeneity across country borders and broad areas
Coherent 3 dimensional GCPs and DEM source
Allows ortho-processing of any image (WV-1, QuickBird, Ikonos, SPOT…)
Large coverage, growing by ~7M km² / year
Acquired nearly anywhere on the globe, in a non-intrusive manner
Update and refresh of data is possible
Allows emergency rapid mapping over denied or remote territory
Alaska Dem Workshop
Notes: <number>
カバレッジ
⇒非公開だそう。（小林さん情報。仕様書は公開されているけど・・・）
GTOPO30は、DTED1と同等。
DTED2, CIB5互換→米軍ほか連合国とのインターオペラビリティに役立つ
縮尺1/50000の地図作製に十分な精度をもつ。R3Dから作製した地図はVMAP0、VMAP1より正確

## Slide 33: The End
Questions? Contact:
miller@spot.com
© Spot Image 2008
<number>
Notes: <number>