## Slide 1: Alaska DEM Workshop
JULY 22, 2008

## Slide 2: Agenda
Sensors
Terrain Models
Accuracy
Grid Spacing
Deliverables
Archive (DEMs, Stereo coverage)
Product

## Slide 3: Agenda cont.
Processor
Ground Control
Geodesy Issues
License
Production Volume
Experience
Pricing
IDIQ Contracts

## Slide 4: Sensor Data
DTM products available utilizing:
  Ikonos
  ASTER
  GeoEye-1

## Slide 5: IKONOS
Digital Terrain Models
  30m posting – 1 arc second
    Ground control not required when block adjusted with multiple image pairs (min. 3)
    11.5m LE90; 25.4m CE90
  5m posting - .2 arc second
    Requires GCPs (1per model)
    3m LE90; 12.2m CE90

## Slide 6: ASTER
Digital Terrain Model
  30m posting - 1arc second
    Utilizing proprietary sensor model
    Ikonos imagery for control
    20m LE90; 25.4m CE90
    DEM examples
Notes: <number>
ASTER products created for areas such as Greenland, Kyrgyzstan, Russia, Canada, etc.

## Slide 7: Greenland
Notes: <number>
25,000km2 (approximately)
Graphic is in geographic projection

## Slide 8: Aasiaat, Greenland
Notes: <number>
ASTER 1x1 arc 20mLE90, 25.4 CE90

## Slide 9: Jakobshavn, Greenland
Notes: <number>
ASTER 1x1 arc 20mLE90, 25.4 CE90

## Slide 10: Upernavik, Greenland
Notes: <number>
ASTER 1x1 arc 20mLE90, 25.4 CE90

## Slide 11: Kyrgyzstan (ASTER)
Notes: <number>
ASTER 1x1 arc 20mLE90, 25.4 CE90
Tashkent area

## Slide 12: Canada (ASTER)
Notes: <number>
ASTER 1x1 arc 20mLE90, 25.4 CE90

## Slide 13: GeoEye-1
Launch date: August 22, 2008
  Data available soon after
Terrain Models
  Product specifications still in work
  Improved vertical accuracy of 5m without GCPs
Notes: Product accuracy for GeoEye-1 terrain models will be verified upon acquiring test data
<number>

## Slide 14: Digital Elevation Models
Generated from proprietary software and/or COTS software
  Extract Digital Surface Models (DSM), edited to Digital Terrain Models (DTM) bare-earth or near bare earth.

## Slide 15: Native Z Accuracy
Ikonos 30m; 1arc DTM
  Vertical accuracy of 14m at the 95% confidence level
ASTER 30m; 1arc DTM
  Vertical accuracy of 24m at the 95% confidence Level

## Slide 16: Improved Z Accuracy
Ikonos 5m; .2 arc DTM
  Vertical accuracy of 4m at the 95% confidence level*
    The .2 arc DTM requires considerably more time to produce
  *Accuracy levels for Ikonos or GeoEye-1 derived models
Notes: <number>
Production time increased due to the increase in post spacing, and time needed to manipulate or edit these to spec.

## Slide 17: R Accuracy
Radial horizontal accuracy of DTMs
  ASTER 1 arc: 25.4 CE90, or 29m at 95% confidence level
  Ikonos 1 arc: 25.4m CE90, or 29m at 95% confidence level
  Ikonos .2 arc: 12.2m CE90, or 14m at 95% confidence level

## Slide 18: Grid Spacing
ASTER DTM:
  1 arc second, 30m
Ikonos DTM:
  1 arc second, 30m
  .2 arc second, 5m

## Slide 19: Deliverables
Standard Products: GeoReference, PrecisionPlus, Pro, and Stereo
  Ikonos DTM
    Formats: USGS DEM, DTED, GeoTIFF, etc.
  ASTER DTM is a non-standard product
    Formats: USGS DEM, DTED, GeoTIFF, etc.
Notes: <number>
All GeoEye products are shipped with a text metadata file, license file, shape files and a JPEG thumbnail image with world file. Shape files show order AOI, delivery component layout, and source image footprints with acquisition geometry.
The metadata includes order parameters as well as source image and product file descriptions. Order parameters include area of interest, spectral bands, and coordinate system, source image description (acquisition date, sun angles and viewing geometry). Product file descriptions include geocoding, spectral bands and coverage area.
Metadata is provided in an ASCII text file and includes GeoEye contact information, order parameters (area of interest, spectral bands, and coordinate system), source image description (acquisition date, sun angles and viewing geometry), and product file descriptions (file names, sizes, and coverage).

## Slide 20: Archive
Archive DEM
Archive Stereo imagery

## Slide 21: Alaska Archive DEMs
Notes: <number>
Approximately 90,00km2

## Slide 22: Alaska Archive Stereo Coverage

## Slide 23: Stereo Coverage <20% CC
Notes: <number>
This graphic shows existing stereo imagery in the archive, with cloud coverage of less than 20%. However, this may not be indicative of suitable (elevation modeling) stereo imagery within the archive.

## Slide 24: Product
We can deliver a DEM product
We can provide stereo imagery for DEM generation
Notes: <number>
Available in various formats such as DTED, GeoTIFF, USGS DEM, etc.

## Slide 25: Processor
To produce DEMs with our stereo data:
  Stereo imagery w/rpcs
  COTS: e.g. SocetSet; PCI Geomatica
    Local Partners:
      Aero-Metric
      ETerra
Notes: <number>
For local Alaska productions of DEMs, we are partners with Aero-Metric and ETerra
We are also partners with I-cubed in Fort Collins, CO

## Slide 26: Special Applications
N/A
Notes: <number>
None that I am aware of. Perhaps this is a service offered through one of our partners such as AeroMetric, ETerra, or ICubed

## Slide 27: Ground Control
Professionally surveyed ground control preferred
  3 GCPs are needed for single stereo pairs
  1 GCP per image in a block adjust of less than 3 image pairs
  .2 arc DTM requires 1 gcp per stereo model

## Slide 28: Ground Control Alternative
Due to the difficulty in acquiring ground control in this region:
  An ASTER block adjust of the entire state with Ikonos control could be used for ground control points needed for DTM production
    Control Points accurate to about 20m CE90

## Slide 29: Geodesy Issues
All using WGS84/ITRF through JPL
  Standard Geoid: EGM96
  Other Geoids as non-standard
  * International Terrestrial Reference Frame
Notes: <number>
EGM96 1m accuracy

## Slide 30: License
Licensing for a state wide DEM would most likely fall under our Tier 3 License category
May be a custom license tier depending on use and pricing
  Flexible to allow for the sharing of data
  Also willing to negotiate with customers with existing data licenses to upgrade to allow for the sharing of data
Notes: <number>
Due to the size of the project, it might be more realistic to put together a custom license

## Slide 31: Production Volume
Ikonos/GeoEye-1
  Major asset due to the 11bit sensor and adjustable gain
    Collection of useable stereo possible in much worse sun angle conditions than an 8bit sensor
Dependent on the collection of suitable stereo imagery
  With a more definitive/specific AOI, a feasibility analysis will be performed producing more useful and accurate data/numbers/statistics
  Clouds, sun angle, and available duty cycle factor into feasibilities resulting in an analysis of yearly production volume
Notes: <number>
Collection feasibility is driven by weather, competition, and access.

## Slide 32: Experience
Greenland ASTER 1arc DTMs
  (25,000+km2)
Alaska Ikonos 1arc DTMs
  (80,000+km2)
Various AOIs throughout the world

## Slide 33: Gustavus, AK
Notes: <number>
WGS84/Geographic projection

## Slide 34: Nenana, AK (Totchaket)
Notes: <number>
WGS84/Geographic projection

## Slide 35: Prudhoe Bay, AK
Notes: WGS84/Geographic projection
<number>

## Slide 36: Lake Clark (North)
Notes: <number>
This slide shows images collected for the Lake Clark elevation models

## Slide 37: Lake Clark (North)
Notes: Resulting 1 arc DEM
<number>

## Slide 38: Tanzania, Africa

## Slide 39: Algeria (.2 arc DEM)
Notes: <number>
One section of 5,000km2 a 5m postings

## Slide 40: Algeria (.2 arc DEM)
Notes: <number>
Zoomed in on Dunes

## Slide 41: Pricing
We are open to negotiation, and can start collections immediately.
  Collection capacity will increase with the successful launch of GeoEye-1
Notes: <number>

## Slide 42: IDIQ Contracts
Prime:
  USGS IDIQ Contract 08CRCN0011
Subcontractor:
  NGA IDIQ Global Geospatial Intelligence Contract, subcontractor to:
    BAE
    Technigraphics, Inc.
    Boeing, Inc.
    Harris Corp.

## Slide 43: Contact Information
Tara Byrnes
  Manager, Partner Development
    byrnes.tara@geoeye.com
    703-480-4602