## Slide 1
Alaska DEM Workshop
July 22-23, 2008 – Anchorage, AK
ASRC Management Services
Cartosat-1 Data Information Provided by:
Dr. Shawana P. Johnson, GISP
and
J. Edward Kunz, GISP
<number>
Notes: <number>

## Slide 2: Project Overview
The State of Alaska is seeking statewide solutions to acquire DEMs with postings between 30 and 10 meters
Alaska needs data
Alaska needs open license to data
Alaska needs data partners
<number>

## Slide 3: ASRC Management Services is Alaska’s Data Partner
ASRC is the Exclusive Provider of Resourcesat & Cartosat Data in the US.
Non-exclusive (only) provider in Mexico & Canada.

## Slide 4: IRS Current Missions
RESOURCESAT-1
CARTOSAT-1
CARTOSAT-2
<number>

## Slide 5: Cartosat-1 Overview
<number>

## Slide 6: Cartosat-1 Overview
Mission Objectives:
To design and develop an advanced 3-axis body stabilized remote sensing satellite for stereo imaging and cartographic applications.
To further stimulate new areas of user applications in the areas of cartographic applications, urban management, national security, and disaster management.
<number>

## Slide 7
Cartosat-1 Overview
<number>
Orbit : | Circular Polar Sun Synchronous
Orbit height : | ~618 km
Orbit inclination : | 98.87°
Orbit period : | 97 min
Number of Orbits per day : | 15
Local Time of Equator crossing : | 10.30 a.m.
Orbital Repeat Cycle : | 126 days
Nominal Wait Time to Acquire Adjacent Path : | 11 days
Max. Wait Time for Revisit : | 5 days
Data Rate : | 105 Mb/s
Solid state storage: | 120GB
Lift-off Mass : | 1,560 kg
Attitude and Orbit Control : | 3-axis body stabilized using Reaction Wheels, Magnetic Torques and Hydrazine Thrusters
Power : | 5 sq m Solar Array generating 1100W (End of Life) Two 24 Ah Ni-CD batteries
Mission Life : | 5 years (launched 05/05/05)

## Slide 8
Cartosat-1 Overview
<number>
CARTOSAT-1
PAN Camera

## Slide 9
Future IRS Missions
Resourcesat-n
Cartosat-n
Radar
HSI
<number>

## Slide 10
Future IRS Missions
Follow on concepts to existing systems
  2009 to 2018
  Many systems already under development
Resourcesat-3 series:
  Increased resolution and more spectral bands:
  Addition of new sensors with 25km swath
Resourcesat-4 series
Increased resolution for Cartosat Series
RISAT – First IRS SAR system
<number>

## Slide 11
DEM Workshop Questions

## Slide 12: 1. Sensor
What sensor do you propose to use for acquisition of source data to be used for DEM production?
    Cartosat-1
<number>

## Slide 13: 2. Model
Are your DEMs produced from the Digital Surface Model (DSM) of the top reflective surface, or do you also produce DEMs from the Digital Terrain Model (DTM) of the bare-earth or near bare-earth -- or a combination or other process?
    ASRC MS provides stereo pairs
<number>

## Slide 14: 3. Native Z accuracy
With minimal ground control, what is the vertical accuracy (Accuracy z) of your DSMs at the 95% confidence level? If you also produce DTMs, what is the vertical accuracy (Accuracy z) of your DTMs at the 95% confidence level?
Use at least one control point every 25sqkm, which provides 9 GCP’s per scene
Accuracy expectation of DSM in the urban can be 6.0m – 9.0m with high accuracy DGPS points
<number>

## Slide 15: 3. Native Z accuracy
With minimal ground control, what is the vertical accuracy (Accuracy z) of your DSMs at the 95% confidence level? If you also produce DTMs, what is the vertical accuracy (Accuracy z) of your DTMs at the 95% confidence level?
GCP’s can be derived with accurate maps for handheld GPS devices
With a couple of GCPs per scene, the vertical DSM accuracy can be 15 meters at 95%, based on the numbers in Table 1
<number>

## Slide 16: Native Z accuracy
Table 1. CARTOSAT -1 accuracy with offset-only correction
<number>

## Slide 17: 4. Improved Z accuracy
For producing digital topographic data of Alaska, would you plan to rely upon satellite or GPS/IMU parameters for accuracy, or would you plan to establish an improved control network? What improved vertical accuracy would you then hope to achieve for your DSMs or DTMs with improved ground control?
An improved control network is necessary.
If increase GCP’s to 25 per scene and DEM accuracy in Urban and Open zones will range 2.5m – 5m.
The onboard GPS/IMU solution is not accurate enough to do DEM extraction (see Table 2).
<number>

## Slide 18: Improved Z accuracy
Table 2. CARTOSAT-1 uncontrolled accuracy
<number>

## Slide 19: 5. R accuracy
What is the (radial) horizontal accuracy (Accuracy r) of your DSMs or DTMs at the 95% confidence level?
Horizontal accuracy of the DEM range 5m – 7m for 9 GCP’s per scene and 3m – 5m for 25 GCP’s per scene.
Horizontal accuracy 10 meters at 95% with a couple of GCPs per scene
<number>

## Slide 20: 6. Grid Spacing
What DEM grid spacing(s) do you normally use or provide?
20m regular grid generated from epipolar pairs is optimum and 10 meters has also been achieved
<number>

## Slide 21: 7. Deliverables
What is delivered with your product, e.g. DEM, DSM, breaklines, contours, orthoimage, ortho radar image, backscatter intensity, etc? Please distinguish between standard products and value-added products.
ASRC provides stereo pairs and thus these products would be completed by a value added provider which provide: - DSM
- Edited DEM
- Ortho imagery
- Breaklines if stereo editing is desired
<number>

## Slide 22: 8. Archive
If you have created DEMs for previous projects or acquired data that can be used to produce DEMs, how much coverage do you have for Alaska? To what specification? What is the status of the data coverage, e.g. produced DEMs, validated data, raw data meeting cloud specs, etc?
Cartosat-1 Alaska Archive
    -Approximately, 1000 stereo pairs
    -June 2005 – April 2008
    -50% are good due to cloud cover
<number>

## Slide 23: 8. Archive
<number>

## Slide 24: Cloud Cover
GDA Corp. has developed a Cloud Cover Extraction Tool which improves the percentage of usable data an additional 25%
- Deliver per pixel cloud & shadow data gap info
- Easily allows removal for DEM
<number>

## Slide 25: 9. Product
Do you deliver a DEM product or do you deliver data that can be made into DEMs by others?
ASRC Management Services provides CARTOSAT-1 Panchromatic 2.5 meter stereo imagery pairs to be used for generation of DEMs by value added processors
<number>

## Slide 26: 10. Processor
If you provide data to generate DEMs, rather than a finished product, what is required to produce DEMs from your data? Have you found certain software that works well? Do you have established processing partners? Is there an opportunity for local Alaska productions of DEMs?
ASRC MS works with value added processing partners
PCI and Genesys are being demonstrated at the workshop due to their recent experience
Most value added processors use PCI-OrthoEngine software
PCI Geomatics has achieved complete certification for its flagship software, Geomatica® to be used for processing data from the CARTOSAT-1 satellite
<number>

## Slide 27: 10. Processor
If you provide data to generate DEMs, rather than a finished product, what is required to produce DEMs from your data? Have you found certain software that works well? Do you have established processing partners? Is there an opportunity for local Alaska productions of DEMs?
ASRC Management Services is a subsidiary of Arctic Slope Regional Corporation and encourages the use of Alaskan labor in the creation of DEMs for the State
ASRC MS currently supports and is involved with the development of GIS Programs in coordination with:
- Several North Slope Borough District High Schools for students to obtain GIS Certification to enter college with credit
- Programs are underway with llisagvik College and the University of Alaska
<number>

## Slide 28: 11. Special Applications
Please identify special applications for planimetric and topographics mapping, and unique value-added applications:
ASRC MS value added processors provide the following standard mapping products:
  -DSM
  -Edited DEM
  -Ortho imagery
  -Breaklines if stereo editing is desired
<number>

## Slide 29: 11. Special Applications
Please identify special applications for planimetric and topographics mapping, and unique value-added applications:
ASRC MS value added processors also provide unique value applications such as:
- 3-D fly through from digital terrain models generated with panchromatic CARTOSAT-1 stereo imagery as well as colorization from Resourcesat
- Change detection and environmental monitoring services are also available
<number>

## Slide 30: 12. Ground Control
What are your requirements for ground control points for acquisition, production, and/or horizontal/vertical accuracy testing? What accuracy would you require both horizontally and vertically for such ground control? Would the existing NGS control be suitable for your needs, or would you require more? If more control is required, what spacing or density of survey points would be needed?
One control point every 25 sqkm, which provides a uniform spread of 9 GCP’s per CARTOSAT scene
<number>

## Slide 31: 13. Geodesy Issues
How do you propose to address geodesy issues such as sparse CORS network, geoid limitations, and the impact of solar activity (k-index) on airborne and ground GPS data collection? Do you have preferences for datums, projections, coordinate systems, and units?
Our Value Added Processors will determine how sparse CORS network, geoid limitations, and solar activity (k-index) on airborne and ground GPS data collection will effect the generation of mapping products from CARTOSAT-1 stereo imagery and data preferences
<number>

## Slide 32: 14. License
What license options are available for your elevation data?
ASRC Management Services is currently working with the Alaska SDMI on an “open license”
Derived products from CARTOSAT-1 imagery such as DEMs may be shared in the state (not for commercial purposes).
<number>

## Slide 33: 15. Production volume
How much area could you produce each year over Alaska?
CARTOSAT-1 imagery collection for the entire State of Alaska will require a minimum of 24-36 months
DEM development running parallel with the imagery collection and cloud cover could take up to 6 years to develop.
<number>

## Slide 34: 16. Experience
Please provide examples if you produced large volumes of data in remote, poorly ground controlled areas in the past.
Horizontal and vertical accuracy of the datasets beyond what can be produced from imagery off of the satellite is in effect proportional to the amount, location and quality of ground control
Our value added processors have been engaged in utilizing CARTOSAT-1 stereo pair imagery since launch to generate DEMs of the nation of India
In this massive project large volumes of data have been produced in areas of minimal or no control. Similar projects are also underway by Euromap
<number>

## Slide 35: 17. Pricing
One goal of the workshop is to bin solutions by cost. A potential binning is <$10M, $10-30M,>$30M. There will be opportunity, either through a future RFP or discussions under NDA, to discuss pricing with potential buyers. Costs should approximate all expenses (tasking, collection, production, licensing to include annual subscription fees, etc.)
A “Satellite Receiving Ground Station” in Alaska that is capable of down linking CARTOSAT-1 and Resourcesat-1 will cost under $5 million per year
<number>

## Slide 36: 17. Pricing
One goal of the workshop is to bin solutions by cost. A potential binning is <$10M, $10-30M,>$30M. There will be opportunity, either through a future RFP or discussions under NDA, to discuss pricing with potential buyers. Costs should approximate all expenses (tasking, collection, production, licensing to include annual subscription fees, etc.)
If imagery costs are 20% of the total project cost in the scenario above, it will require an investment based on the Value Added Community charges for DEMs
The estimated cost to “Acquire & Download Cartosat-1 Data in Alaska” is approximately $3.26/per sqkm vs. $8.60 per sqkm if Cartosat-1 Data is purchased from the recorder
<number>

## Slide 37: 18. IDIQ Contracts
Are you a prime contractor and/or subcontractor on existing government IDIQ contracts? If so please list the contract(s) as well as name(s) of prime contractor(s) for which you serve as subcontractor.
ASRC MS is The Prime Contractor and subcontractor on numerous IDIQ type contracts such as:
The US Department of Agriculture Prime Vendor Contract
Partner in the NJVC (manages multimillion dollar IDIQ for NGA)
<number>

## Slide 38: All Cartosat-1 DEM Publications
www.asrcms.com
<number>

## Slide 39: Thank You!
For More Information Contact:
Dr. Shawana P. Johnson, GISP
shawana@globalinsights.com
216-525-0600
~or~
J. Edward Kunz, GISP
ed.kunz@asrcms.com
301-837-5354
<number>